## Slide 1
ECO-LOOP BUILDING AGENTS
AI that thinks before your building wastes energy.
An open-source LLM closes the control loop on a live EnergyPlus simulation — set-points injected into the running instance, savings proven against an identical baseline.
PROBLEM STATEMENT
ID — «fill in from portal»
Title — Eco-Loop Building Agents: autonomous closed-loop building control (Honeywell Hackathon · Question 1)
Theme — «fill in from portal»
PS Category — Software
TEAM
Student Name (registered on portal) — Pranav Kumar
Student ID — «fill in from portal»
IN THE REPOSITORY
Closed-loop source · baseline and runtime-generated .idf models · savings dashboard · docs/ARCHITECTURE.md · 392 passing tests
MEASURED ON REAL ENERGYPLUS — NOT PROJECTED
32.1%
ENERGY SAVED
115.5 kWh
29.1%
PEAK CUT
16.2 → 11.5 kW
79 → 0
COMFORT VIOLATIONS
of 80 occupied steps
✓ COMFORT MAINTAINED · ASHRAE-55 PMV BAND HELD ALL DAY
EnergyPlus 26.1 · summer week · 192 timesteps of 15 min
Agent run and fixed-schedule baseline execute the identical code path, weather and occupancy — a controlled experiment, reproducible from two CLI commands.
EnergyPlus 26.1
Llama 3.3 70B via Groq
MCP server
FastAPI + SSE
React + Recharts
392 tests passing

## Slide 2: ECO-LOOP BUILDING AGENTS
Buildings waste energy because their controls cannot think. Ours reasons — every fifteen minutes.
THE PROBLEM
✕
Buildings burn ~40% of global energy
and remain a primary driver of carbon emissions.
✕
Building management systems run fixed schedules
blind to weather, occupancy and grid carbon intensity.
✕
Control is reactive, not anticipatory
comfort is corrected only after occupants have complained.
79 of 80
occupied timesteps outside the comfort band — measured on the fixed-schedule baseline in EnergyPlus.
OUR SOLUTION
✓
AI SUPERVISOR
Llama 3.3 70B reads live telemetry and sets the control policy.
✓
ENERGYPLUS DIGITAL TWIN
Set-points injected into the running instance — no restart, no file rewrite.
✓
REACTIVE SAFETY GUARD
Every action clamped in code to hard comfort and equipment limits.
✓
MCP TOOL LAYER
The same six tools serve the agent and any external MCP client.
✓
LIVE SAVINGS DASHBOARD
Eight panels streaming telemetry, reasoning and kWh saved.
WHAT MAKES IT DIFFERENT · baseline and agent run the identical code path, weather and occupancy — so the saving is a controlled experiment, not a demo

## Slide 3: TECHNICAL APPROACH
One closed loop: sense → reason → clamp → actuate, inside the running simulation.
ENERGYPLUS DIGITAL TWIN
small_office.idf · EPW weather
pyenergyplus runtime API
SENSOR TELEMETRY
zone temp · outdoor · occupancy
CO₂ · power · PMV
every 15-min timestep
LLM SUPERVISOR
llama-3.3-70b via Groq
6 JSON-schema tools
on cadence · ~0.8 s
REACTIVE GUARD
clamps to hard comfort
and equipment limits
every step · microseconds
FORWARD INJECTION
set-points written to
EnergyPlus actuators
live instance · no restart
CLOSED LOOP — the next timestep's telemetry already reflects the action just written. 35,040 steps (a full simulated year) completed end to end.
EVIDENCE STORE
SQLite: runs · timesteps · decisions. 39,690 telemetry rows and 5,021 decisions persisted, with rationale, latency and guard overrides.
API LAYER
FastAPI — 14 REST endpoints plus a Server-Sent Events stream and per-run CSV export. The dashboard is a pure reader.
MCP SERVER
The agent's own ToolRegistry served over stdio, so an external MCP client drives the identical six tools.
Python 3.12
EnergyPlus 26.1
pyenergyplus
Groq · Llama 3.3
MCP
FastAPI
React + Vite
Recharts
392 tests

## Slide 4: FEASIBILITY AND VIABILITY
It already runs — and it is engineered to fail safely.
✓
RUNS TODAY
Real EnergyPlus 26.1 and real Groq calls, measured at 465–2,449 ms per supervisory decision. Two CLI commands reproduce the headline number.
✓
TESTED
392 automated tests pass — 161 backend (pytest) and 231 frontend (vitest), including the EnergyPlus thread bridge and forward injection.
✓
EVIDENCED
39 recorded runs · 39,690 telemetry rows · 5,021 decisions, each with its rationale and latency. Every run exports to CSV.
RISK → OUR ANSWER
Model latency on a 35,040-step year
↓
Two-tier control. The guard runs every step in microseconds; the LLM runs on a cadence and only chooses the policy. The loop never waits on a model.
A hallucinated or unsafe set-point
↓
Safety lives in code, not in a prompt. Every action is clamped to hard comfort and equipment limits, and each override is recorded as guard_clamped.
Hosted API rate-limits, times out, or fails
↓
Bounded retries → circuit breaker → baseline fallback through the same guard. One 192-step run completed with 44 of 48 supervisory calls degraded and zero crashes.
Logs and telemetry exceed any context window
↓
logsummary.py compacts before prompting: severity filtering, warning de-duplication and statistical windowing of long traces.

## Slide 5: ARTIFACTS
The live dashboard on the real run: 32.1% less energy, zero comfort violations.
Live telemetry — zone temperature against the set-point band · agent vs baseline energy · PMV inside the ASHRAE-55 band
Every decision explains itself — and the guard's overrides are on the record
32.1%
kWh saved vs baseline
0
comfort violations
192/192
steps, zero crashes
48.5 kg
CO₂ avoided in 2 days
AGENT DECISION — VERBATIM FROM THE RUN LOG
“The zone is unoccupied and will remain so for the next 4 steps, so we can set back the temperature and turn off the lighting to save energy.”
set_control_policy · setback · 19.0 / 20.5 °C · 849 ms · llama-3.3-70b-versatile
REPRODUCE THE HEADLINE NUMBER
python cli.py --scenario summer_week --controller baseline --simulator energyplus --days 2
python cli.py --scenario summer_week --controller rule --simulator energyplus --days 2 --compare <id>
Artifacts: backend/ (24 modules) · frontend/ (9 components) · small_office.idf + runtime-generated variants · docs/ARCHITECTURE.md · 392 tests

## Slide 6: RESEARCH AND REFERENCES
WHY THIS SOLUTION WINS — six claims, each backed by something in the repository.
REAL AI
An open-weight Llama 3.3 70B reasons over live telemetry and emits a policy through native tool-calling.
REAL SIMULATION
EnergyPlus 26.1 driven through its runtime API — actuators written mid-run, not a file regenerated between runs.
EXPLAINABLE
Every decision persists its rationale, tool call, latency and any guard override. The dashboard shows them live.
SAFE
A deterministic guard clamps every action to hard comfort and equipment limits, so a hallucinated set-point cannot reach the building.
SCALABLE
The simulator sits behind a Protocol and the model is named in .env — neither vendor is locked in; the MCP server opens the tools to any client.
PRODUCTION-READY
392 passing tests, a typed API, an evidence store and CSV export — a controlled experiment anyone can re-run.
RESEARCH AND REFERENCES
STANDARDS
• Fanger PMV / PPD thermal comfort — ISO 7730 Annex D and ANSI/ASHRAE Standard 55; implemented in app/comfort.py.
• EnergyPlus Weather (EPW) hourly format — parsed in app/sim/weather.py.
SIMULATION ENGINE
• EnergyPlus 26.1 and its runtime Python API (pyenergyplus), NREL — github.com/NREL/EnergyPlus/releases
• Baseline model derived from the distribution example MovableExtInsulationSimple.idf.
MODEL AND PROTOCOL
• Groq inference API serving open-weight Llama 3.3 70B (llama-3.3-70b-versatile) — console.groq.com
• Model Context Protocol — official Python SDK (mcp ≥ 1.0), wrapping the agent's own ToolRegistry.
Full design rationale, sequence and data-flow diagrams, database schema and design decisions D1–D11: docs/ARCHITECTURE.md